## Slide 1
Evolutions possibles ICRH de WEST
24 septembre 2019
J.Hillairet, L.Colas, P.Mollard, G.Lombard, J-M.Bernard

## Slide 2: Contexte de la réunion
Pour répondre à cette demande, je souhaite que l’on fasse ensemble un point technique sur le système ICRH de WEST :
· Statut du système : puissance max injectée par antenne, fiabilité, compatibilité technique LHCD, etc.
· Potentiel du système en l’état : puissance max possible sur les plasmas de WEST actuels et estimation en mode H, indépendamment du rayonnement et autres problèmes de contrôle
· Impact attendu d’un dépôt de bore sur les protections latérales : contribution de cette source par rapport aux autres, résultats d’ASDEX Upgrade avant le dépôt et après le dépôt sur une antenne similaire en terme de puissance totale rayonnée ?
· Modifications des antennes de WEST : pour augmenter la résistance de couplage ?
Je propose de faire une première réunion pour explorer toutes les pistes (sans analyse des ressources et de planning à ce stade), la semaine du 16 au 20 septembre. On validera les éventuelles actions à lancer lors d’un prochain COPIL HCD.

## Slide 3: Take-home message: there are margins for improvements
ICRH System Improvements
  Q2 coupling resistance normalization
  Phase control
Plasma Scenario Improvements
  LSN vs USN shows large uncertainties with LFS plasma radial location
Impurity Production
  Prad during ICRH sometimes larger than with LH.
  Measurable contribution of IC limiters to core contamination.
  Low-Z material  may reach similar frad during ICRH and LH.
Local Gas puffing recipes
  Tbd, especially if better pumping in C5
From coupling POV:
4 MW IC
demonstrated
6 MW IC (60 s)
seems achievable
Impurity production needs to be reduced
Operation domain/recipes

## Slide 4
Système ICRH – Bilan C4 et évolutions possibles

## Slide 5: C4 Statistics (preliminary)
Main C4 Results
  RF plant reliable due to good maintenance during shutdown
  All three antennas operational simultaneously on plasma few times 3 MW/few seconds, 4.2 MW peak.

## Slide 6: C4 Statistics (preliminary)
Main C4 Results
  RF plant reliable due to good maintenance during shutdown
  All three antennas operational simultaneously on plasma few times 3 MW/few seconds, 4.2 MW peak.
  Up to 2.4 MW (2 antennas) in // with LH (but impurity problem)

## Slide 7: C4 Statistics (preliminary)
Main C4 Results
  RF plant reliable due to good maintenance during shutdown
  All three antennas operational simultaneously on plasma few times 3 MW/few seconds, 4.2 MW peak.
  Up to 2.4 MW (2 antennas) in // with LH (but impurity problem)
  Load resilience confirmed

## Slide 8: C4 Statistics (preliminary)
Main C4 Results
  RF plant reliable due to good maintenance during shutdown
  All three antennas operational simultaneously on plasma few times 3 MW/few seconds, 4.2 MW peak.
  Up to 2.4 MW (2 antennas) in // with LH (but impurity problem)
  Load resilience confirmed
Incidents:
  Regular maintenance performed on plant
  Delay on Q4 startup due to cabling defects
  Few problems with the hydraulic system (cylinders, position encoder)  All solved during maintenance
  One voltage probe out of order on Q1 (cable?) Investigations during S4
  One capacitor of Q2 can’t move since its servopack is out of order. Obsolete component, bought online second hand.  Full update of the servomotors and control systems during S4

## Slide 9: ICRF Coupling during C4 (preliminary)
Average coupling resistance for WEST C4 is
  between 0.8 -1.0 Ω for Q1 and Q4
  Closer to 0.6 for Q2
Clear difference between LSN and USN plasmas for all antennas
Still clear difference with Q2
Plasma control

## Slide 10: Plasma control
Comparison btw VACTH and EQUINOX equilibrium (500kA/3.6T plasmas)
  En USN, différence de l’ordre de 15mm sur le Rext.
  En LSN, différence de .. 40mm !
 Would explain coupling difference measured btw LSN and USN?
From N. FEDORCZAK (18/09)
Conclusion: probably margin for coupling improvements in C5

## Slide 11: Plasma control
Ecart dans la position R_ext entre NICE et VACTH.
  En moyenne il y a un écart de 2cm, la valeur calculé par VACTH est plus grande.
Evolution en fonction du numéro de choc
  la différence négative montre que R_ext_vacth > R_ext_nice.
Pour la configuration USN l’écart est légèrement plus faible.
  Les points rouges (distance point X négative) sont USN, les points bleus (positifs) sont en LSN.
Bonne soirée,
Jorge
Jorge Morales 23/09/219

## Slide 12: Radial position drift with time ex: #55015
Plasma LCFS moves away from the antennas
  Coupling resistances drop
  Leads to power regulation and/or trips
  Corrections in progress (week 38)
-14mm

## Slide 13: Q2 Coupling Resistance
Q2 coupling resistance has been found different from Q1 during the C3 campaign
Coupling resistance is deduced from voltages and power measurements
   Power measurements recalibrated during S3, still difference clearly remains.
In C4, the coupling of Q1 and Q4 has been found equivalent.
   seems to indicate a peculiarity of Q2
Conclusion: difference in Q2 voltage probe calibration as most probable explanation
Such behaviour could be explained by a dist. diff. to LCFS ~ 10-15 mm
 Can’t be explained by mechanical differences (cf. measures), since:
- strap/FS distance is 30.5 mm (-1.6/ +2.2)
- Antenna radial positions checked during S3
C3b: Rc vs distance antenna/LCFS

## Slide 14: WEST Antenna voltage probe calibration procedure
Probes are calibrated at low frequency (~1 MHz)
Calibration data are then extrapolated to nominal frequencies (48 to 63 MHz)
Probe coupling is *very* sensitive to its depth in its port
~ 3.3 dB/mm from modelling/measurements
Q2 was the first antenna to be assembled and calibrated
  Probes have been disassembled then reinstalled *after* the calibration (for welding access)  mechanical error between 1st and 2nd assembly?
Probe head depth
0

## Slide 15: How Q2 voltage probe calibration should be modified to match Q1 and Q4?
From similar shots from Friday 13/09
Voltages compared btw Q2 and Q4 during 4.06 et 4.16 for pulses 55108 to 55114
  Caveat: VSWR not exactly identical (frozen capacitor positions)
 | VQ2 | VQ4 | VQ2/VQ4
Gauche Haut | 15 | 11.95 | 1.25
Gauche Bas | 19.9 | 16.1 | 1.23
Droit Haut | 16.7 | 12.3 | 1.35
Droit Bas | 13.9 | 16.5 | 0.84
VQ2 ~ 1.25 x VQ4 pour 3 sondes
NB: 20log10(1.25) = 1.94 dB
Correction proposée: -1.94 dB pour ces 3 sondes
 Erreur de positionnement équivalent à ~ 0.6 mm (crédible)

## Slide 16: Test of the proposed modification (to be validated)
#55144 vs #55145
 Q2 Rc increase (consequence of reduced voltages)  No more power regulation and power ~ Q4
Risks: If the cause of voltage differences between Q2 and other antennas is different than a pure calibration problem, it may increase capacitor voltages and currents to:
27 kV x 1.25 = 33.8 kV
915 A x 1.25 = 1143.8 A
Eventually: Measurements could be performed during S4 at low RF power on two antennas (side by side) with machine under vacuum.
Conclusion: validation of this modification?

## Slide 17: Quelle puissance peut on atteindre?
Si on prend comme référence Q4
  2 MW / ant possible si Rc > 1.6 Ohm soit 6 MW pour 3 antennes
Power regulation limit: Pmax~ 1.2 Rc

## Slide 18: WEST Antenna Toroidal Phase Automatic Regulation
Phase control started since #54626 (but not on all antennas/at the same time)
  OK for Q4
  Better control for Q2
  Does not work on Q1 yet
Conclusion: still margin for improvements. Need to update hardware.

## Slide 19: Impurity production vs phase WEST #55192
Failure in Q2 phase control leads to:
  Radiated power increase
  WI radiance increase on lateral limiters but not on divertor

## Slide 20: Effect of LH on IC Coupling Resistance
LH power increases the Rc average by 0.25 ohm
  But important dispersion: sometime opposite effects measured
  Database biased: few shot with LH and Q2

## Slide 21: Antenna Modifications
Reducing the radial gap between antenna limiters and Faraday screen (few mm)?
Q: Can we improve coupling by modifying the antennas?
Some ideas:

## Slide 22
Impact attendu d’un dépôt de bore sur les protections latérales

## Slide 23: Impact de la boronisation sur la puissance rayonnée (bulk)
frad=100%
frad=60%
frad=50%
Phase tests

## Slide 24: Outline, take-away message
Need more margins on Psep to get « useful » H-mode on WEST
  Prad,bulk higher with ICRH than with LH at similar power.
  Especially when both systems are combined at high power.
Experimental indications of contamination by IC side limiters
  Effects of boronization on Prad,bulk in IC-heated discharges.
  On some sessions, the divertor source evolution is anti-correlated with Prad,bulk.
  Phase scans on WEST.
  Effect of LH-IC combination was observed on IC limiter sources.
Clearer demonstration: W vs B-coated limiter comparison
  Prad reduction was measured in ASDEX upgrade.
  B-coatings presently used on AUG. No operational issue reported in the litterature.
  Detrimental effect of W limiters on contamination observed on EAST.
  Indications for WEST.

## Slide 25: Radiated power fraction on 20/09/2019
Outer divertor
Target plasma
  LSN, Ip=500kA. Nl3~4-4,5e19
  3 ICRF launchers and LH1 grill energized sequentially at similar power.
  PLH1 Background (0,1MW,1,5MW) added on shot to shot basis.
  Then 3 antennas grouped.
  Detached plasma in first pulses, no visible consequence on Prad,bulk.

## Slide 26: Effet of LH power on IC radiated fraction?
  DPrad,bulk/PICRH close to LH in absence of LH background.
  DPrad,bulk/PICRH generally higher in presence of LH background.
  Yet large scatter, strong IC antenna dependance. Hidden parameter?
  Caveat: only Q2 antenna monitored by DVIS.

## Slide 27: Radiation in ICRF-only discharges, week 36
  Statistics with ICRH alone
  Mainly USN pulses.
  Boronization on 02/09.
  Between 03/09 (late) and 06/09 (late): 1 session in USN, 4 in LSN, no ICRH
  Frad slightly higher far from boro.
  But frad less than 50% is possible with ICRH alone far from boronization… because ICRH was not used?
  More bolometry signal when Q2 is used, even on 03/09. Measurement arftefact?

## Slide 28: Scaling of frad,bulk in IC-heated plasmas week 36
Fit 03/09: Prad,bulk=0,49*PW+0,34*(PQ1+PQ4)+0,57*PQ2
Fit 06/09: Prad,bulk=0,71*PW+0,43*(PQ1+PQ4)+0,60*PQ2
? Bolometry during Q2 ?
Main boro.
effect
Boro effect preserved?

## Slide 29: USN/LNS comparison on 18/09
  Boronization on 16/09.
  17/09: LSN plasmas heated by LH and ICRH (3-antennas).
  18/09: ICRF-heated pulses in LSN at 700kA,
  #55170: Switch to USN (clean divertor) and repeat.
  Prad,bulk/Ptot: some reduction in ohmic, more marginal with ICRH
  Prad,div/Ptot: reduction by 20-30% both in ohmic and IC.

## Slide 30: Radiated power fraction on 31/07
Target plasmas
  Nl3=4,5-5e19
  ICRH only.
  Ip and Bt scans.
  Good IC heating efficiency, except for off-axis heating
frad increases with PICRH
  35-50% in ohmic, 60-75% with 1MW.
  Different from LH behaviour.
  Indicative of IC-specific contamination?
Parametric dependance
  Slightly higher at Ip=500kA than higher Ip.
  Slightly higher for off-axis heating (ITOR=1150A)

## Slide 31: Divertor visible spectroscopy during ICRH
  Inner: Both DI and WI line radiance decrease during ICRH.
  Outer: ~10× lower intensities, DI line radiance increases, WI radiance slightly decreases
  Time delays, overshoot in divertor dynamics.
  Lower conducted power during ICRH?
Inner divertor
Outer divertor
Ip=700kA; ITOR=1250A

## Slide 32: WI brightness inner divertor: parametric variation
Most intense divertor source
Trends opposite to frad variation.
  Decreases with larger PICRH
  Larger decrease for off-axis heating (ITOR=1150A).
  Weak at Ip=500kA, increases with larger Ip.
Cannot explain higher contamination during ICRH

## Slide 33: WI brightness, outer divertor: parametric variation
  Signal levels ~10 times below inner divertor.
  Very low for Ip=500kA, ITOR=1250A
  Generally decrease with ICRF power.
  Slight increase for some LODIVOU channels and off-axis heating.

## Slide 34: Main chamber W sources
Only antenna Q2 right limiter reacts to ICRH
  Sensitive to Q1 antenna (magnetically connected to side limiter), not Q4.
  Higher signals for off-axis heating and (Ip, ITOR)=(500kA, 1200A).
  Prompt time response (no delay/overshoot).
Caveat: leading W sources in chamber probably missed !
  Active antennas Q1 and Q4 not observed by visible spectroscopy.
  Observed antenna Q2 used only at the begining of the session.

## Slide 35: IC antenna limiter mainly reacts to local IC antenna

## Slide 36: WEST #55192
Inner divertor
leading W source
Outer divertor
IC Q2
Antenna limiter

## Slide 37: LH-IC combination on IC limiters in C3b
GD=f(nl, PLH)
  Proxy: DId brightness on ant. limiter
  Larger at high density  IC coupling
  Increases faster than nl with PLH
  W penetration also evoloves with nl
Yeff=g(Te,VQ2)
  Proxy for Yeff: line ratio WI/ DId
  Proxy for IC near field amplitudes: VQ2
#53778
#53923
#53778
#53923

## Slide 38
B-coated side limiters in 2012:
 Difference of about 50% of cW rise
just because of toroidal limiters
 Rough estimate: all ICRF limiters account at
least for 70% of cW rise in AUG, the rest
from other W structures.
W- vs. B-coated limiter comparison in 2012
V. Bobkov et al.
Workshop WEST
Aix, 2014!
 VUV spectroscopy: measured gain on Prad,W is about 50% of applied ICRF power.

## Slide 39
Sometimes higher gain, depending on configuration
DPrad,W> PICRH

## Slide 40: Issues with W at outer mid-plane on EAST
| PAGE 40
  Before 2018:
      W only on upper divertor,
      C on LH limiters
      USN/LSN ohmic pulse comparison.
  After 2018:
      W limiters installed ed on LH launcher.
      USN /LSN comparison repeated
      WUSN/WLSN decreased by 3,5.
      Estimated limiter contribution: 25% in OH.
  Little ICRH power from the magnetically connected antenna has very large effect on W production compared to all others heating systems
ASIPP

## Slide 41: Q4am, bon emplacement pour une antenne bas-Z
  L’auto-polarisation du plasma par rectification de gaine HF se propage sur de longues distances le long des lignes de champ ouvertes issues des antennes ICRH actives.
   éviter les connexions magnétiques aux autres PFCs-W.
  Q4 est relativement éloignée des autres objets côté faible champ,
  L’objet le plus proche est le LPA, qui peut être reculé franchement.
  On ne pourra toutefois pas éviter des connexions de Q4 avec le baffle, qui existent aussi avec les autres antennes.
Q4am

## Slide 42: Outlook
Need more margins on Psep to get « useful » H-mode on WEST
  Prad,bulk higher with ICRH than with LH at similar power.
  Especially when both systems are combined at high power.
Either the present experimental indications from WEST and AUG are convincing enough…
  We should then boronize the side limiters on all 3 ICRF antennas.
  Potentiel gain: frad,bulk similar with ICRH and LH.
  B-coated limiters presently used on AUG. No operational issue reported in the litterature.
…Or they are not
  It is then our duty to make a clear experimental comparison on WEST by ourselves.
  Preference: boronize Q4 and keep Q2 with W coatings for DVIS measurements.
  Potential reduction of Prad,bulk increases with the number of B-coated antennas.
Additional remarks
  Boron is already introduced on purpose every week on WEST.
  Clear effect of W limiters on EAST plasmas.
  Low-Z impurities will be present on ITER whatsoever. IC antennas surrounded with Be.
  Long shutdown is the right moment to work on IC limiters.

## Slide 43: SPARE

## Slide 44
Dirvertor sources
Assumptions on inner div
  On average Гw=2.1018atm/s
  Radial extention ~ 4cm
  Toroidal extention = 360°
Assumptions on outer div
  On average Гw=1017atm/s
  Radial extention ~ 10cm
  Toroidal extention = 360°
Remarks
  Similar with all heating schemes
  Some screening effect
Source estimation

## Slide 45
Limiters sources
Assumptions
  On average Гw=1017atm/s
  Poloidal extention ~ 50cm
  Toroidal extention ~ 10cm
  3 ICRF antennas ON  6 limiters
Remarks
  Negligible when not powered
  No screening effect
Source estimation

## Slide 46: L’ICRH, souvent « inutile » pendant C3b
  Sur les chocs les plus performants de la campagne C3b, la quasi-totalité de la puissance ICRH injectée était rayonnée par le plasma (vs. 50-60% pour LH).
  Dans l’état actuel des choses la puissance ICRH contribue peu (voire pas)
      À la transition du plasma en mode H.
      aux flux de chaleur sur les monoblocs de divertor.