## Slide 1
Evolutions possibles ICRH de WEST
24 septembre 2019
J.Hillairet, L.Colas, P.Mollard, G.Lombard, J-M.Bernard

## Slide 2: Contexte de la réunion
Pour répondre à cette demande, je souhaite que l’on fasse ensemble un point technique sur le système ICRH de WEST :
· Statut du système : puissance max injectée par antenne, fiabilité, compatibilité technique LHCD, etc.
· Potentiel du système en l’état : puissance max possible sur les plasmas de WEST actuels et estimation en mode H, indépendamment du rayonnement et autres problèmes de contrôle
· Impact attendu d’un dépôt de bore sur les protections latérales : contribution de cette source par rapport aux autres, résultats d’ASDEX Upgrade avant le dépôt et après le dépôt sur une antenne similaire en terme de puissance totale rayonnée ?
· Modifications des antennes de WEST : pour augmenter la résistance de couplage ?
Je propose de faire une première réunion pour explorer toutes les pistes (sans analyse des ressources et de planning à ce stade), la semaine du 16 au 20 septembre. On validera les éventuelles actions à lancer lors d’un prochain COPIL HCD.

## Slide 3: Take-home message: there are margins for improvements
ICRH System Improvements
  Q2 coupling resistance normalization
  Phase control
Plasma Scenario Improvements
  LSN vs USN shows large uncertainties with LFS plasma radial location
Impurity Production
  Prad during ICRH sometimes larger than with LH.
  Measurable contribution of IC limiters to core contamination.
  Low-Z material  may reach similar frad during ICRH and LH.
Local Gas puffing recipes
  Tbd, especially if better pumping in C5
From coupling POV:
4 MW IC
demonstrated
6 MW IC (60 s)
seems achievable
Impurity production needs to be reduced
Operation domain/recipes

## Slide 4
Système ICRH – Bilan C4 et évolutions possibles

## Slide 5: C4 Statistics (preliminary)
Main C4 Results
  RF plant reliable due to good maintenance during shutdown
  All three antennas operational simultaneously on plasma few times 3 MW/few seconds, 4.2 MW peak.

## Slide 6: C4 Statistics (preliminary)
Main C4 Results
  RF plant reliable due to good maintenance during shutdown
  All three antennas operational simultaneously on plasma few times 3 MW/few seconds, 4.2 MW peak.
  Up to 2.4 MW (2 antennas) in // with LH (but impurity problem)

## Slide 7: C4 Statistics (preliminary)
Main C4 Results
  RF plant reliable due to good maintenance during shutdown
  All three antennas operational simultaneously on plasma few times 3 MW/few seconds, 4.2 MW peak.
  Up to 2.4 MW (2 antennas) in // with LH (but impurity problem)
  Load resilience confirmed

## Slide 8: C4 Statistics (preliminary)
Main C4 Results
  RF plant reliable due to good maintenance during shutdown
  All three antennas operational simultaneously on plasma few times 3 MW/few seconds, 4.2 MW peak.
  Up to 2.4 MW (2 antennas) in // with LH (but impurity problem)
  Load resilience confirmed
Incidents:
  Regular maintenance performed on plant
  Delay on Q4 startup due to cabling defects
  Few problems with the hydraulic system (cylinders, position encoder)  All solved during maintenance
  One voltage probe out of order on Q1 (cable?) Investigations during S4
  One capacitor of Q2 can’t move since its servopack is out of order. Obsolete component, bought online second hand.  Full update of the servomotors and control systems during S4

## Slide 9: ICRF Coupling during C4 (preliminary)
Average coupling resistance for WEST C4 is
  between 0.8 -1.0 Ω for Q1 and Q4
  Closer to 0.6 for Q2
Clear difference between LSN and USN plasmas for all antennas
Still clear difference with Q2
Plasma control

## Slide 10: Plasma control
Comparison btw VACTH and EQUINOX equilibrium (500kA/3.6T plasmas)
  En USN, différence de l’ordre de 15mm sur le Rext.
  En LSN, différence de .. 40mm !
 Would explain coupling difference measured btw LSN and USN?
From N. FEDORCZAK (18/09)
Conclusion: probably margin for coupling improvements in C5

## Slide 11: Plasma control
Ecart dans la position R_ext entre NICE et VACTH.
  En moyenne il y a un écart de 2cm, la valeur calculé par VACTH est plus grande.
Evolution en fonction du numéro de choc
  la différence négative montre que R_ext_vacth > R_ext_nice.
Pour la configuration USN l’écart est légèrement plus faible.
  Les points rouges (distance point X négative) sont USN, les points bleus (positifs) sont en LSN.
Bonne soirée,
Jorge
Jorge Morales 23/09/219

## Slide 12: Radial position drift with time ex: #55015
Plasma LCFS moves away from the antennas
  Coupling resistances drop
  Leads to power regulation and/or trips
  Corrections in progress (week 38)
-14mm

## Slide 13: Q2 Coupling Resistance
Q2 coupling resistance has been found different from Q1 during the C3 campaign
Coupling resistance is deduced from voltages and power measurements
   Power measurements recalibrated during S3, still difference clearly remains.
In C4, the coupling of Q1 and Q4 has been found equivalent.
   seems to indicate a peculiarity of Q2
Conclusion: difference in Q2 voltage probe calibration as most probable explanation
Such behaviour could be explained by a dist. diff. to LCFS ~ 10-15 mm
 Can’t be explained by mechanical differences (cf. measures), since:
- strap/FS distance is 30.5 mm (-1.6/ +2.2)
- Antenna radial positions checked during S3
C3b: Rc vs distance antenna/LCFS

## Slide 14: WEST Antenna voltage probe calibration procedure
Probes are calibrated at low frequency (~1 MHz)
Calibration data are then extrapolated to nominal frequencies (48 to 63 MHz)
Probe coupling is *very* sensitive to its depth in its port
~ 3.3 dB/mm from modelling/measurements
Q2 was the first antenna to be assembled and calibrated
  Probes have been disassembled then reinstalled *after* the calibration (for welding access)  mechanical error between 1st and 2nd assembly?
Probe head depth
0

## Slide 15: How Q2 voltage probe calibration should be modified to match Q1 and Q4?
From similar shots from Friday 13/09
Voltages compared btw Q2 and Q4 during 4.06 et 4.16 for pulses 55108 to 55114
  Caveat: VSWR not exactly identical (frozen capacitor positions)
 | VQ2 | VQ4 | VQ2/VQ4
Gauche Haut | 15 | 11.95 | 1.25
Gauche Bas | 19.9 | 16.1 | 1.23
Droit Haut | 16.7 | 12.3 | 1.35
Droit Bas | 13.9 | 16.5 | 0.84
VQ2 ~ 1.25 x VQ4 pour 3 sondes
NB: 20log10(1.25) = 1.94 dB
Correction proposée: -1.94 dB pour ces 3 sondes
 Erreur de positionnement équivalent à ~ 0.6 mm (crédible)

## Slide 16: Test of the proposed modification (to be validated)
#55144 vs #55145
 Q2 Rc increase (consequence of reduced voltages)  No more power regulation and power ~ Q4
Risks: If the cause of voltage differences between Q2 and other antennas is different than a pure calibration problem, it may increase capacitor voltages and currents to:
27 kV x 1.25 = 33.8 kV
915 A x 1.25 = 1143.8 A
Eventually: Measurements could be performed during S4 at low RF power on two antennas (side by side) with machine under vacuum.
Conclusion: validation of this modification?

## Slide 17: Quelle puissance peut on atteindre?
Si on prend comme référence Q4
  2 MW / ant possible si Rc > 1.6 Ohm soit 6 MW pour 3 antennes
Power regulation limit: Pmax~ 1.2 Rc

## Slide 18: WEST Antenna Toroidal Phase Automatic Regulation
Phase control started since #54626 (but not on all antennas/at the same time)
  OK for Q4
  Better control for Q2
  Does not work on Q1 yet
Conclusion: still margin for improvements. Need to update hardware.

## Slide 19: Impurity production vs phase WEST #55192
Failure in Q2 phase control leads to:
  Radiated power increase
  WI radiance increase on lateral limiters but not on divertor

## Slide 20: Effect of LH on IC Coupling Resistance
LH power increases the Rc average by 0.25 ohm
  But important dispersion: sometime opposite effects measured
  Database biased: few shot with LH and Q2

## Slide 21: Antenna Modifications
Reducing the radial gap between antenna limiters and Faraday screen (few mm)?
Q: Can we improve coupling by modifying the antennas?
Some ideas:

## Slide 22
Impact attendu d’un dépôt de bore sur les protections latérales

## Slide 23: Impact de la boronisation sur la puissance rayonnée (bulk)
frad=100%
frad=60%
frad=50%
Phase tests