## Slide 1
Status of the ICRH System in WEST C4 (preliminary)
WEST Task Force Meeting – 26/09/2019
J.Hillairet, P.Mollard, G.Lombard, F.Durand, L.Colas, J-M.Bernard

## Slide 2
Main C4 Results
(so far!)

## Slide 3: WEST C4 Statistics (preliminary)
Main C4 Results (so far)
  RF plant reliable due to good maintenance during shutdown
  All three antennas operational simultaneously on plasma few times 3 MW/few seconds, 4.2 MW peak.

## Slide 4: WEST C4 Statistics (preliminary)
Main C4 Results (so far)
  RF plant reliable due to good maintenance during shutdown
  All three antennas operational simultaneously on plasma few times 3 MW/few seconds, 4.2 MW peak.
  Up to 2.4 MW (2 antennas) in // with LH (but impurity problem limits duration)

## Slide 5: WEST C4 Statistics (preliminary)
Main C4 Results (so far)
  RF plant reliable due to good maintenance during shutdown
  All three antennas operational simultaneously on plasma few times 3 MW/few seconds, 4.2 MW peak.
  Up to 2.4 MW (2 antennas) in // with LH (but impurity problem limits duration)
  Load resilience confirmed

## Slide 6: WEST C4 Statistics (preliminary)
Main C4 Results (so far)
  RF plant reliable due to good maintenance during shutdown
  All three antennas operational simultaneously on plasma few times 3 MW/few seconds, 4.2 MW peak.
  Up to 2.4 MW (2 antennas) in // with LH (but impurity problem limits duration)
  Load resilience confirmed
Incidents:
  Regular maintenance performed on plant
  Delay on Q4 startup due to cabling defects
  Few problems with the hydraulic system (cylinders, position encoder)  All solved during maintenance
  One voltage probe out of order on Q1 (cable?) Investigations during S4
  One capacitor of Q2 can’t move since its servopack is out of order. Obsolete component, bought online second hand.  Full update of the servomotors and control systems during S4

## Slide 7: ICRF Coupling during C4 (preliminary)
Average coupling resistance for WEST C4 is
  between 0.8 -1.0 Ω for Q1 and Q4
  Closer to 0.6 for Q2
Clear difference between LSN and USN plasmas for all antennas
Still clear difference with Q2
Plasma control

## Slide 8: Higher Coupling found in USN Uncertainties on plasma frontier
Comparison btw VACTH and EQUINOX equilibrium (500kA/3.6T plasmas)
  In USN, difference on Rext is of the order of 15mm
  In LSN, difference on Rext can reach 40 to 60 mm…
 Would explain coupling difference measured btw LSN and USN?
From N. FEDORCZAK and Jorge MORALES
Conclusion: probably margin for coupling improvements in C5

## Slide 9: Higher Coupling found in USN Distance to cut-off density is lower in USN
# 54902 (USN) vs 54903 (LSN): 500 kA, nl 4.1019 m-3
1.5 Ω
0.5 Ω
Rext is (supposed to be) similar
Cut-off distance is different : ~ 20 mm (from reflectometry)
43 vs 19 mm
18 vs 14 mm

## Slide 10: Radial position drifts with time ex: #54719
Plasma LCFS moves away from the antennas
  Coupling resistances drop
  Leads to power regulation and/or trips
  Corrections in progress (week 38)
>10 mm shift toward HFS

## Slide 11: Radial position drifts with time ex: #55015
Plasma LCFS moves away from the antennas
  Coupling resistances drop
  Leads to power regulation and/or trips
  Corrections in progress (week 38)
-14mm

## Slide 12: Boronization helps reducing radiated fraction
frad=100%
frad=60%
frad=50%
Phase tests
  Borononization performed on Mondays
  IC sessions on Tuesday and Friday evenings: some data to be compared
  Caveat: results heavily depend on antennas phasing, but anyway, a clear tendency appears

## Slide 13
Q2 Coupling Resistance
Will the mystery come to an end?

## Slide 14: Q2 Coupling Resistance
Q2 coupling resistance has been found different from Q1 during the C3 campaign
Coupling resistance is deduced from voltages and power measurements
   Power measurements recalibrated during S3, still difference clearly remains.
In C4, the coupling of Q1 and Q4 has been found equivalent.
   seems to indicate a peculiarity of Q2
Conclusion: difference in Q2 voltage probe calibration as most probable explanation
Such behaviour could be explained by a dist. diff. to LCFS ~ 10-15 mm
 Can’t be explained by mechanical differences (cf. measures), since:
- strap/FS distance is 30.5 mm (-1.6/ +2.2)
- Antenna radial positions checked during S3
C3b: Rc vs distance antenna/LCFS

## Slide 15: WEST Antenna voltage probe calibration procedure
Probes are calibrated at low frequency (~1 MHz)
Calibration data are then extrapolated to nominal frequencies (48 to 63 MHz)
Probe coupling is *very* sensitive to its depth in its port
~ 3.3 dB/mm from modelling & measurements
Q2 was the first antenna to be assembled and calibrated
  Probes have been disassembled then reinstalled *after* the calibration (for welding access)  mechanical error between 1st and 2nd assembly?
Probe head depth
0

## Slide 16: How Q2 voltage probe calibration should be modified to match Q1 and Q4?
From reproducible shots from Friday 13/09
Voltages averaged btw Q2 and Q4
  Caveat: VSWR not exactly identical (some frozen capacitor positions at that time)
 | VQ2 | VQ4 | VQ2/VQ4
Left Upper | 15 | 11.95 | 1.25
Left Bottom | 19.9 | 16.1 | 1.23
Right Upper | 16.7 | 12.3 | 1.35
Right Lower | 13.9 | 16.5 | 0.84
VQ2 ~ 1.25 x VQ4 for 3 probes
NB: 20log10(1.25) = 1.94 dB
Proposed correction until end of C4: -1.94 dB for 3 probes
Equivalent to a positioning error ~ 0.6 mm (credible)
Additional investigations during next shutdown

## Slide 17: Test of the proposed modification
#55144 vs #55145
 Q2 Rc increase (consequence of reduced voltages)  No more power regulation and power ~ Q4
Risks: If the cause of voltage differences between Q2 and other antennas is different than a pure calibration problem, it may increase capacitor voltages and currents to:
27 kV x 1.25 = 33.8 kV
915 A x 1.25 = 1143.8 A
Risk considered acceptable until the end of C4

## Slide 18
Toroidal Phase Control

## Slide 19: WEST Antenna Toroidal Phase Automatic Regulation
Phase control started since #54626 (but not on all antennas/at the same time)
  OK for Q4 (quite resilient)
  Better control for Q2 (but get easily distracted)
  Does not work on Q1 yet
Conclusions:
  Still margin for improvements (for sure).
  Investigations ongoing. Need to update hardware (tbc).

## Slide 20: Impurity production vs phase WEST #55192
Failure in Q2 phase control leads to:
  Radiated power increase
  WI radiance increase on lateral limiters but not on divertor
From L.Colas

## Slide 21
IC and LH
Status: from « it’s complicated » to « it's getting better and better »

## Slide 22: Effect of LH on IC Coupling Resistance
LH power increases the Rc average by ~0.25 ohm
  But important dispersion: sometime opposite effects measured
  Database biased: few shot with LH and Q2

## Slide 23: Copper Impurities (only?) currently limiting the High Confinement Scenario
61% of IC radiated
49% of LH radiated
2.2 MW IC
4.2MW LH

## Slide 24
(Preliminary) Summary

## Slide 25: Status of the ICRH System during C4 (preliminary) summary
All 3 ICRH antennas available on plasma
IC power alone on specific scenarios :
  4.2 MW peak achieved on USN plasma
  Coupling different in 500kA USN vs LSN. Investigations ongoing.
H-mode scenario:
  Low density and coupling resistance, meaning ~1 MW/ant
  Max so far: 2.2 MW IC with 2 antennas in // with 4.2 MW LH
Toroidal phase control progress, but still work to do to make it reliable